| Safe Work Method Statement (SWMS) Part 1 |
| --- |
| Activity: Painting | SWMS #: |
| Business Name: | ABN: |
| Business Address: |
| Business Contact: | Phone #: |
| SWMS Approved by: Employer / PCBU / Director / OWNER. |
| Name: |
| Signature: | Date: |
| Person/s responsible for ensuring compliance with SWMS: |
| Person/s responsible For reviewing the SWMS: |
| Relevant workers consulted in the development, approval and communication of this SWMS. | All Persons involved in the task must have this SWMS communicated to them before work commences. |
| Name | Signature | Date | Daily Tool Box Talks will be undertaken to identify, control and communicate additional site hazards. |
|  |  |  | Work must cease immediately if incident or near miss occurs. SWMS must be amended in consultation with relevant persons. |
|  |  |  | Amendments must be approved by ______________ and communicated to all affected workers before work resumes. |
|  |  |  | SWMS must be made available for inspection or review as required by WHS legislation. |
|  |  |  | Record of SWMS must be kept as required by WHS legislation (until job is complete or for 2 years if involved in a notifiable incident). |
| Principal Contractor Details (The builder or the organisation you are working for.) |
| Principal Contractor (PC): | Project Name: | Date SWMS provided to PC: |
| Project Address: |
| Project Manager (PM): | PM Signature: | CONTACT PH. #: |
| SWMS Scope: This SWMS covers general painting procedures using hand tools, power tools, and spray gun. |

| This work activity involves the following “High Risk Construction Work” |
| --- |
| ☐ Confined Spaces |  Mobile Plant | ☐ Demolition | ☐ Asbestos |
| ☐ Using explosives | ☐ Diving work | ☐ Artificial extremes of temperature | ☐ Tilt up or pre-cast concrete |
| ☐ Pressurised gas distribution mains or piping chemical, fuel or refrigerant lines energised electrical installations or services |
| ☐ Structures or buildings involving structural alterations or repairs that require temporary support to prevent collapse |
|  Involves a risk of a person falling more than 2m, including work on telecommunications towers |
| ☐ Working at depths greater than 1.5 Metres, including tunnels or mines | ☐ Work in an area that may have a contaminated or flammable atmosphere |
| ☐ Work carried out adjacent to a road, railway or shipping lane, traffic corridor | ☐ In or near water or other liquid that involves risk of drowning |
| Likelihood | Insignificant | Minor | Moderate | Major | Catastrophic | Score | Action | HIERARCHY OF CONTROLS | Most Effective |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |  |  |  |  |
| Likely | 2 Moderate | 3 High | 3 High | 4 Acute | 4 Acute | 4A Acute | DO NOT PROCEED. |  |  |
| Possible | 1 Low | 2 Moderate | 3 High | 4 Acute | 4 Acute | 3H High | Review before commencing work. |  |  |
| Unlikely | 1 Low | 1 Low | 2 Moderate | 3 High | 4 Acute | 2M Moderate | Maintain control measures. |  |  |
| Rare | 1 Low | 1 Low | 2 Moderate | 3 High | 3 High | 1L Low | Record and monitor. |  | Least Effective |
| Personal Protective Equipment (PPE): Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. |
| Foot Protection | Hearing Protection | High Visibility | Head Protection | Eye Protection | Face Protection | Hand Protection | Protective Clothing | Breathing Protection | Sun Protection | fall Arrest | Rings, watches, jewellery that may become entangled in machines must not be worn. Long and loose hair must be tied back. |
|  |  | ☐ |  |  | ☐ |  |  |  |  | ☐ |  |

| Job Step | Potential Hazard/s | IR | Control Measures to Reduce Risk | RR | Responsible Person |
| --- | --- | --- | --- | --- | --- |
| Inherent Risk-rating (IR) Residual Risk-rating (RR) |
| Planning & preparation | Lack of consultation may lead to potential outcomes for personal injury, property damage &/or environmental incident. | 3H | Liaise with Principal Contractor to establish the following on-site systems and procedures are in place and take note of: Health and Safety rules Induction for all workers – site specific and toolbox meetings Supervisory arrangements Communication arrangements All relevant workers are appraised for required competencies & for any pre-existing medical conditions if working in remote or isolated locations. PPE required Site plans – showing no go zones for pedestrians Traffic Management Plan Exclusion Zones Risk Assessments SWMS and JSA’s Injury reporting procedures Hazard reporting procedures. | 2M |  |
|  | Contact with hazardous materials | 4A | Seek information from a competent person regarding the presence of lead and/or asbestos. If there is a presence of lead and/or asbestos, for this task, ensure there are separate, dedicated SWMS and that all workers/employees have relevant training and licensing. | 2M |  |
|  | Heritage listing requirements | 3H | Ensure permits associated with Heritage Listed buildings are available on site. | 2M |  |
|  | Remote and/or isolated work - personal Injury from delay in emergency assistance to remote workers | 4A | A ‘Buddy’ system is utilised for high-risk tasks undertaken in remote locations or working in isolation. A procedure is developed and in place for regular contact with people working remotely or in isolation, The procedure should identify: Travel itineraries, locations, scheduled contact persons and times Sufficient supplies of water, food, fuel & supplies needed An emergency response Appropriate Vehicles Safety equipment including first aid. | 2M |  |
| Training and Capabilities | Lack of training or the assessment of capability may lead to personal injury, property damage &/or environmental incident. | 3H | Ensure all persons entering site have a General Construction Induction Card (white card). Ensure all relevant workers have undertaken training and/or received instruction in the use of control measures. Include: All workers are trained in this SWMS Correct use of equipment including selecting, fitting, use, care of and maintenance Use of supervision where required (e.g. new starters or new equipment) Using hazardous chemicals/atmospheres Reporting procedures for incidents Ensure supervisors, foremen etc. are suitably experienced in the type work to be conducted Correct use of all tools used. | 2M |  |
| Transporting paints & equipment | Environmental incident / spills | 3H | Ensure all chemicals container lids are securely fitted Secure so paints cannot move / become damaged / spill during transit. | 2M |  |
|  | Struck by moving objects | 3H | Ensure to isolate main vehicle cabin from carrier area with a fixed barrier or transport paint and equipment on a trailer / tray back Secure so paints / equipment cannot move during transit. | 2M |  |
|  | Securing ladders / planks |  | The overhang of horizontally stored ladders / planks beyond the support points of the rack should be minimised The support points should be constructed of material such as wood or rubber-covered pipe to minimise the effects of vibration, chafing and road shock Securing the ladder / planks to each support point will greatly reduce the damaging effects of road shock Ensure the vehicle is suitable for the type and size of the ladder / planks The ladder / planks must be restrained to prevent unacceptable movement during all expected conditions while in transit: The load restraint system must meet the Regulation Performance Standards (see relevant authority) Check with the relevant authority on the rules and regulations on attaching warning devices on long loads. NOTE: A ladder rack attached to your work vehicles is the best tool for the job. Secure the ladder / planks to the rack so that is has no chance of falling from the vehicle and can protect the ladder / planks from damage, and other commuters on the road while in transit. |  |  |
|  | Property & public safety |  | Ensure ladders / planks are well secured to the transport vehicle: Walk to the side of the vehicle to see how well centered the ladder / plank is from front to back Adjust the ladder / plank so that the majority of its length is centered directly above the truck from front to back Tie a red flag (at least 300mm x 300mm) on the end of any ladder / plank that extends beyond the rear of the vehicle If transporting at night, ensure ladder / plank that extend beyond the vehicle > 1m have a red warning light or two reflectors attached to the end of the ladder. NOTE: For ladders / planks that extend beyond 1m of the front or rear of the vehicle, check your state regulations for specific allowable overhangs. Slide the ladder / plank to the side of the ladder rack if additional ladders will be loaded Load each additional ladder in the same manner as the first Tie each side of each ladder / plank to the frame of the ladder rack using appropriate tie down method (e.g. straps) Ensure strap are placed over the sides of the ladders / planks and in between the rungs of the ladders to keep extension ladders from moving forward or backward. |  |  |
| Assess onsite conditions | Lack of a clear assessment may lead to personal injury, property damage &/or environmental incident. | 3H | Assess conditions at site on arrival. Ensure: | 2M |  |
|  |  |  | Ensure site-specific induction is undertaken (include location of amenities, first aid facilities, emergency plans and evacuation points, incident reporting, communication, contact persons etc.) Assess mobile phone reception (alternative emergency communications procedures in place if no reception available) | Work site is exactly as detailed in Terms of Agreement or contract Suitable access for all equipment required Suitable space for operation of equipment Suitable lighting, including night-works (include flood lighting and operator head lamps as applicable). |  |  |
|  |  |  | Conduct risk assessment to identify potential hazards such as: Work at heights (above 2m) Lighting Ventilation Presence of hazardous materials such as asbestos, lead, silica etc. Location of existing services (heating, water, pipes, electrical leads) Dust Temperature etc. Exposed electrical switchboards/power points Duration of manual handling tasks (such as working with arms above shoulder height). |  |  |
| Work area set up | Fire | 3H | Ensure no ignition sources in area. Note: Ignition sources include pilot lights, stoves, heaters, cigarettes, matches/lighters, grinding, welding, power points, lighting, light switches, radio transmitters, mobile phones etc. | 2M |  |
|  | Muscular stress / musculoskeletal disorder (MSD) | 3H | Sufficient lighting Ensure materials / equipment is as close to work area as possible Use mechanical aids as much as possible. | 2M |  |
|  | Work adjacent to road & public safety | 4A | Park working vehicle in driveway or allocated parking to avoid travelling across roads when delivery working equipment If setting up roadside – comply with local laws and permits Erect any barriers & signage necessary to keep others safe and aware. | 2M |  |
|  | Contact with mobile plant or passing vehicle | 3H | Check constantly for changing hazards while working and monitor work position at all times. Ensure: High visibility clothing worn at all times Do not stand behind reversing vehicles Allow sufficient distance from plant during operation (allow sufficient room for equipment failure – such as arm/boom failure or plant rollover) No work is conducted in established “no go zones” for pedestrians Alertness at all times. Listen for: Reversing alarms/beepers Calls from Plant Operators Safety/warning signs, Spotters, traffic barriers etc. must be obeyed as required Work positions should be in clear sight of plant operators Follow traffic management plan requirements. NOTE: Some traffic management plans may say that pedestrians have right-of-way. Never assume this. Make visual and verbal contact with plant operator as required. | 2M |  |
|  | Property damage & other worker/public safety | 3H | Ensure equipment is not placed in areas where they may be run over, damaged or exposed to water (unless rated for wet environments). Keep power leads up off the ground and out of the way Protect existing surfaces, where required, by placing and taping plastic on the surface. Establish Spray Zone: | 2M |  |
|  |  |  | Provide signs/barriers to designate spray zone Ensure zone is large enough to protect persons/property from exposure to vapours/fumes/overspray Restrict entry Provide screening/tunnelling where possible | Isolate ignition sources at least 6m from spray zone (including light switches, motors, smoking, hazardous chemicals, hot works etc.) Provide local exhaust mechanical ventilation where possible Remove all other persons, equipment, and hazardous chemicals. |  |  |
|  | Slips, trips & falls on the same level | 3H | Work area is clean and uncluttered. Equipment Location: Where it will not become a tripping hazard All air hoses are located so they are not across walkways, roadways, thoroughfares etc. Electric leads should be as short as possible. Identify all hazards when setting up ladders / trestles. Consider: Ground/floor surface condition Where ground surfaces may change level Check design to ensure that the equipment will support a specified load – or ‘duty rating’. This must be clearly stated on the item Weather conditions (rain, wind loads, fog, dew) Experience of workers Use all height-access equipment as per manufacturer’s instructions and for its designed purpose. | 2M |  |
|  | Working at heights above 2m. | 3H | If working on EWPs or scaffolding, for this task, ensure there are separate, dedicated EWP/Scaffolding SWMS and that all workers/employees have relevant training and licensing. Identify and control the dangers of using Compressed Air while working at height: Set up jobs to minimise the need for air hoses to be used while working on ladders/trestles/scaffolds Do not set up the compressor unit on a scaffold or trestle. | 2M |  |
|  | Fall from ladder | 3H | Do not use excessively long ladders (example, more than 9m) – use EWP for these tasks. Work positioning. Ensure: Load rating of at least 120kg Correct size and length for job No damage, clean and dry Secured to work site (base and top) Metallic, wire- reinforced or conductive ladders should be avoided around live electrical equipment Face ladder when ascending/descending. Ensure 3 points of contact remain on ladder at all times Ensure only 1 person working from each ladder. | 2M |  |
|  | Fall from platform ladder | 3H | Ensure: Trestle back undamaged If unfolding type, chains, rivets etc. are undamaged and functional Suitable height hand rail (900mm) Triangular flat plate bracing Correct size for job (platform level) Non-slip treads Large feet with non-slip mouldings Non-slip platform of sufficient strength for persons, tools and equipment Industrial rating. | 2M |  |
|  | Fall from trestle | 3H | Trestles must: Be rated for proposed weight and span Have an overhang of at least 150 mm and not more than 250mm at each end and be “locked” together. Example - clamped near the centre span to prevent individual movement Have an unobstructed surface width of at least 450mm (two planks wide) Must be matched pairs i.e. the rungs should be equivalent heights and spacing. Ensure the scaffold is on firm level ground with the feet properly supported Never use loose building material to support the weight of the scaffold. | 2M |  |
|  | Noise | 3H | Locate equipment (compressor) where it will be the least noise hazard to others. | 2M |  |
|  | Contact with electricity | 3H | All power tools and leads are Tested and Tagged and are current Isolate electrical power if required Cover/mask electrical sockets/GPO’s | Pre-inspect equipment If equipment is damaged, do not use. Take out of service, apply Lock-out/tag-out (LOTO) procedures and inform supervisor immediately. | 2M |  |
|  |  |  | Check for overhead wires or other electrical installations before setting up ladders / trestles. Use caution using aluminium / steel extension roller handles when near external power lines Note: Turning off electricity to the property at the main switchboard does not turn off the electricity supply from the street. Overhead service lines and the cables supplying the switchboard will still be live. Do not touch any of these live overhead electrical lines or supply cables. Ensure power is switched off when sanding or painting around power points, light fittings or other energised electrical components Where electrical hazards are identified, a qualified electrical contractor should be engaged to eliminate or control this risk. |  |  |
|  | Working environment | 3H | Outdoors, ensure: Suitable protective clothing Sun brim on hard hat Safety glasses - UV Rated Use 30+ sunscreen on exposed skin areas Adequate drinking water Access to shade during breaks Adequate breaks Check weather conditions – do not work in extreme weather. | Indoor damp atmosphere, ensure: Wear suitable protective clothing and breathing protection Adequate ventilation and air circulation – add fans, open windows and doors Heaters to dry surfaces. | 2M |  |
|  | Contact with hazardous chemicals / substances / atmospheres | 3H | Ensure current Material/Safety Data Sheets (M/SDS) are obtained for all hazardous chemicals/substances and accessible on site. PPE as prescribed in M/SDS for decanting is provided and used Ensure suitable respiratory protection and cartridge is selected as directed in SDS, inspect: | 2M |  |
|  |  |  | Filters, seals, and valves Ensure filter and respirator are compatible Ensure respiratory equipment is regularly cleaned and maintained | Inspect PPE for any sign of damage Replace filters if damaged, when resistance increases and as per manufacturer’s instructions. |  |  |
|  |  |  | Operate and inspect spray gun as per manufacturers instructions. Including: |  |  |
|  |  |  | Unit and pump are grounded Spray gun is correctly attached to the air supply hose Electrical leads are grounded and not placed in areas where they may be damaged / run over etc. Tip guard in place Trigger lock in place and functional | All high pressure connections are tight No pressure leaks (do not test with hands) Hoses are in good condition with no signs of wear Hoses are not placed on or near sharp objects that could damage them and result in a hose bursting during use. |  |  |
|  |  |  | Ensure the air compressor is suitable capacity (size and safe working pressure) for task. Inspect equipment. Check: |  |  |
|  |  |  | Hoses, pipes, fittings are rated the same maximum psi as unit and are compatible and correct size Hoses and couplings are not damaged Hoses and tools are correctly fitted and secured (clips in place) Fly wheels, pulleys, belts, chains, sprockets and other moving parts are guarded | Safety valves and cut-offs are present, undamaged and clear of obstructions (Usually a ring pull. Air discharge should stop when ring is released.) Unit grounded (if required) No water/moisture in air tank Check oil levels Outlet valves, if fitted are closed. |  |  |
| Surface preparation including sanding, caulking & patching | Use of power tools and/or air compressor | 3H | Follow the Pre-operational checklist in the manufacturer’s operational manual. Set-up and operate as per manufacturer’s instructions. Refer to step 8 Use of power tools and air compressor. | 2M |  |
|  | Contact with electricity | 4A | Locate and maintain awareness aware of any power lines when working on ladders / trestles Locate and maintain awareness aware of any extension leads. | 2M |  |
|  | Repetitive, sustained tasks | 3H | Ensure: Avoid overreaching Job rotation Sufficient breaks | Ensure tool handles: Comfortable grip No sharp edges Have extendable handles. | 2M |  |
|  | Debris / dust | 3H | Ensure eye, breathing protection and protective clothing is worn. | 2M |  |
|  | Falling objects | 3H | Use caution when working at elevated levels: Avoid using tools when working from a ladder Consider use of elevated work platform (EWP) Use tool lanyards to pass tools to persons at height and ensure tools cannot fall onto workers below Ensure kickboards installed on elevated work areas to prevent tools falling off. | 2M |  |
|  | Slips, trips & falls on the same level | 3H | Ensure: Non slip foot protection are worn Secure footing Safe access and egress Sufficient lighting Free of tripping hazards i.e. excess material Complete visibility of work area. When using plastic to protect floor surfaces cover the plastic with drop sheets, wet plastic will become very slippery. | 2M |  |
|  | Caulking & patching products | 3H | Follow directions of use Consult M/SDS for the product Use PPE as per the product safety sheet | Use with adequate ventilation Chemical resistant gloves for prolonged exposure. | 2M |  |
| Mixing and applying paints | Muscular stress / musculoskeletal disorder (MSD) | 3H | Use the correct tool for each stage of the task Use alternate arms for painting, and direction of painting strokes (vertical/ horizontal) when possible Take regular breaks Do not overreach Maintain good posture avoiding awkward twisting and side bending Practice stretching throughout the shift Ensure adequate lighting | Ensure tool handles have: Comfortable grip No sharp edges Are cylindrical and approx. 4cm in diameter Allow wrist to remain straight Grip length approx. 12cm Adequate lighting - The rendering process is best carried out in the early or late times of the day to achieve the required finish. | 2M |  |
|  | Contact with electricity | 4A | Locate and maintain awareness aware of any power lines when working on ladders / trestles Locate and maintain awareness aware of any extension leads. | 2M |  |
|  | Exposure to hazardous chemicals / substances: occupational asthma, skin sensitisation, respiratory diseases, cancer | 3H | Adequate ventilation and other necessary safety precautions should be provided when using solvent-based products, particularly in enclosed spaces. Wear safety goggles to protect eyes from splashing and overspray Check SDS for respirator requirement, such as a half-face with organic cartridge: Latex paint: No respiratory equipment if well ventilated, long pants/sleeves or coveralls Oil-based: Air-purifying half face mask with organic vapour cartridge, safety glasses, coveralls (tyvek) Isocyantate-containing: Supplied air, hooded tyvek suit Ensure spraying is not done in upward direction, as this directs spray into breathing zone and face Mix minimum quantity of paint necessary Ensure flammable liquid containers are grounded during pouring Ensure chemical-impervious gumboots and protective clothing is worn. | 2M |  |
|  | Falling objects | 3H | Use caution when working at elevated levels: Avoid using tools when working from a ladder Consider use of elevated work platform (EWP) Use tool lanyards to pass tools to persons at height and ensure tools cannot fall onto workers below Ensure kickboards installed on elevated work areas to prevent tools falling off. | 2M |  |
|  | Slips, trips & falls on the same level | 3H | Maintain good housekeeping cleaning up spills regularly Tools are kept tidy not causing a trip hazard | Non slip foot protection are worn Secure footing when wetting the wall Do not overspray when dampening the surface. | 2M |  |
|  | Fluid under pressure | 3H | Ensure: Spray gun hoses are routed as straight as possible to avoid kinking Any water condensate is drained from the compressed air system Satisfactory pressure for the operation of the spray gun Spray gun is held perpendicular to the surface area being sprayed at all times, with the air line held back away from the item Work arranged to minimise exposure. Be aware of wind direction, avoid spraying into wind (rotate work – not operator) Staggered work positions to avoid overspray of the operators Spray gun pointed only at the work – never at yourself or another person Spraying is not done in upward direction, as this directs spray into breathing zone and face. | 2M |  |
|  | Air under pressure | 3H | Using high-pressure air can cause serious injury NEVER use compressed air for blowing dust off skin or clothing NEVER point the air hose at persons, or use to clean clothing, shoes, or any part of the body. | 2M |  |
|  | Spills | 3H | Spills: Shut off all possible sources of ignition Contain using sand and earth to prevent runoff into drains and waterways Collect and seal in properly labelled drums for disposal Ensure adequate ventilation. | For larger spills: Contain, take up with inert absorbent material (e.g. sand, soil) Place in secure labelled containers for disposal. | 2M |  |
|  | Public and other worker safety | 3H | Remove all non-essential persons from area Barricade area and place caution signs as needed. | 2M |  |
| Using power tools & air compressor | Noise | 3H | Wear hearing protection, ensure it is: Worn by all persons throughout the period of exposure to noise Suitable for the type of working environment and the work tasks Comfortable and correctly fitting for the worker Regularly inspected and maintained to ensure it remains in good, clean condition. | 2M |  |
|  | Fire / explosion | 3H | Do not operate power tools in explosive atmospheres (i.e. presence of flammable liquids, gases or dust). | 2M |  |
|  | Contact with electricity | 3H | Ensure: Use tools only for the purpose specified by the manufacturer Use tools as per Safe Operating Procedures and/or operators manual Ensure instruction manual accessible and read by all persons operating equipment Never carry electrical tools by power cord Do not use power cord to pull equipment from power socket Unplug tool when not in use Check for damage or faults regularly during operation. Examples, if excessive vibration occurs, stop using immediately. | 2M |  |
|  | Struck by moving part – unsecured hose whipping | 3H | Check pressure and thermal regulating gauges regularly Avoid bending/kinking hoses Regularly check hoses are not being damaged or getting caught up/ tangled etc. during use Do not leave compressor plugged in to power source when not in use NEVER drag attached tools by the air hose. If the air hose gets caught on something, don’t pull on the hose. Go find the problem and release the hose. | 2M |  |
|  | Vibration / Muscular stress / MSD | 3H | Avoid over reaching Job rotation | Avoid any twisting, awkward positions and side-bending Do not use excessive force when operating power tools. | 2M |  |
| On completion | Slips, trips, falls causing injury | 3H | Clean up tools and any waste ensuring the site is left in clean and tidy condition Clean debris and ensure it is removed from area. | 2M |  |
|  | Contact with electricity | 3H | Disconnect power tool/extension leads from power point before winding up, so that you don’t get a shock if the lead is damaged Inspect leads and power equipment for damage If safe to do so, remove isolation locks/tags and test appliance for function. Ensure: That no electrical appliances, light fittings, cables etc. have been damaged If damage suspected, do not turn power back on, seek advice from licensed electrician Reconnect services as required. Notify homeowner and/or site supervisor. | 2M |  |
|  | Contamination of waterways and water catchment | 3H | All paint products may be harmful to aquatic life. Prevent contamination of sewers, drains and waterways: Dispose of dried waste materials in approved landfill Dried empty cans can be recycled and should be disposed of via council metal recycling facilities Do not pour any leftover product down the drain Retain in a marked sealed container for future use of disposal via special chemical waste collection programs. | 2M |  |
|  | Public safety | 3H | If acceptable, remove barricades, contact supervisor and return as agreed. Store leftover paint in the original container with the label intact. | 2M |  |

| Emergency Response - Call 000 immediately. |
| --- |
| If work is to be conducted on a construction site (or a site controlled by another Employer / PCBU) follow the site-specific Emergency Management Plan. Ensure: Adequate numbers of first aid trained staff are on site when working at heights occurs First aiders are trained and competent in managing injuries associated with demolition until emergency services arrive All rescue equipment is in good condition, available for use and in close proximity to the work site. | Ensure workers have access to: First aid kit/supplies First Aid trained personnel familiar with Resuscitation and emergency response for electric shock M/SDS Communication devices (check mobile phones will have service in area) Suitable fire protection equipment. |
| Safe Work Method Statement (SWMS) Part 2 |
| Formal Training, Licences required for workers undertaking this task: | Relevant Legislation & Codes of Practice Retain only the legislation references applicable to your state of operation for this SWMS. |
| Delete or add as relevant Licence to Perform High Risk Work (operating certain plant, equipment) Certificate III in Painting and Decorating White WHS Construction Induction Card (or equivalent) Competent in operation of make/model of plant Emergency procedures – emergency response PPE Traffic Management Plans | Commonwealth, NSW, QLD, ACT Work Health and Safety Act 2011 Work Health and Safety Regulations 2011 Northern Territory Work Health and Safety (National Uniform Legislation) Act 2011 Work Health and Safety (National Uniform Legislation) Regulations SA, Tasmania Work Health and Safety Act 2012 Work Health and Safety Regulations 2012 Codes of Practice: Safe Work Australia (2011): Construction Work First Aid in the Workplace Managing the Risk of Falls at Workplaces Managing the Risk of Plant in the Workplace Managing Noise and Preventing Hearing Loss in the Workplace How to Manage Work Health and Safety Risks Hazardous Manual Tasks Managing Risks of Hazardous Chemicals Managing Electrical Risks in the Workplace Managing the Work Environment and Facilities WHS Consultation, Cooperation & Coordination | Victoria: Occupational Health & Safety Act 2004 Occupational Health & Safety Regulations 2007 Compliance Codes: WorkSafe Victoria (2008): Compliance Code: Communicating OHS Across Languages First Aid in the Workplace Prevention of Falls in General Construction Workplace Amenities and Work Environment Codes of Practice: WorkSafe Victoria (1990): No. 13: Building and Construction Workplaces (2000): No. 25: Manual Handling (1995): No. 19: Plant (1998): No. 23: Plant (Amendment No. 1) (2004): No. 29: Prevention of Falls in Housing Construction (2000): No. 24: Hazardous Substances Western Australia Occupational Safety & Health Act 1984 Occupational Safety & Health Regulations 1996 Codes of Practice: |
| Details of Supervisory Arrangements for workers undertaking this task: |  |  |
| Delete or add as relevant Suitably qualified supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc. Reporting systems |  |  |
| Details of: regulatory permits/licenses Engineering Details/Certificates/WorkCover. Approvals: |  |  |
| Delete or add as relevant Local council permits Authorisation to work Confined Space Permit Building Approvals EPA approvals/permits Certain plant to be registered with State Authority PPE to comply with relevant Australian Standards |  |  |
|  | Plant/Tools/Equipment List for the job. | Reference Documents |
|  | (Make & Model) |  |

| Safe Work Method Statement (SWMS) Part 3 |
| --- |
| This SWMS has been developed in consultation and cooperation with employee/workers and relevant Employer/Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including risk control measures, safe work instructions and Personal Protective Equipment described. |
| Overall Risk Rating after Controls | 1 Low | 2 Moderate | 3 High | 4 Acute |
| Employee/Worker Name | Job Role / Position | Signature | Date | Time | Employer/PCBU/ Supervisor |

| Review: Ensure all controls are reviewed as per the following: If controls fail to reduce risk adequately When changes to the workplace or work activity occur that create new / different risks where controls may no longer be effective New hazards identified After an incident involving work activities relevant to this SWMS During consultation with relevant persons indicate review is needed A Health and Safety Representative (HSR) requests a review in line with the requirements of the legislation. | Monitor: To ensure controls are implemented and monitored effectively: Toolbox /pre-work meetings will be undertaken Relevant persons will be consulted on hazards and contents of SWMS, work plans and other applicable information Control measures will be monitored throughout works: *Spot checks *Consultation *Scheduled audits Corrective actions will be recorded and rectified in a timely manner SWMS will be reviewed and updated accordingly (in consultation with relevant persons). |
| --- | --- |
| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Name: |  |  |  |  |  |  |  |  |  |  |
| Initial: |  |  |  |  |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |  |  |  |  |

# Text boxes

DO NOT:

- Attempt to move or extend ladder when on it

- Slide down stiles

- Step up or down two or more rungs at a time